## Slide 1: Software Engineering PROJECT
BY
VIDUR NAYYAR
(GROUP 5)

## Slide 2: Central HUB
Main part of the star topology network.
Components used :
  Arduino Mega
  344MHz RF Transmitter
  315MHz RF Receiver
User interface implemented at the HUB.
Made to be flexible and controlled thorugh server, voice, manual input, over the net or directly through any mobile application.
Notes: - All signals from the server are accepted through the serial port to the hub and then communicated to the various devices to perform the work.
-Tx nd Rx of different frequency to avoid any interference coz we are using a duplex system.
-Used basic RX nd TX instead of xbee so that I could implement my own protocol for communicating & makes it more cost efficient.
-

## Slide 3: Light-Controller Node
Controls the brightness of the light and also retrieves the feedback about the brightness from the light.
Components used :
    2 ATTiny 85 Micro-controller
    RF Receiver 344MHz
    RF Transmitter 315MHz
    Sensor (Light Dependent Resistor)
    Light
Divided into two parts:
1) Receiver and Controller circuit | 2) Sensing and Feedback circuit
Notes: -Perfect synchronization between the HUB and the receiver circuit and Feedback circuit
Handshake method used in which the transmitter sends out a signal/command to the Light-Controller Node.
This command is received by the receiver circuit and the appropriate INFRARED code is selected and used to control the music player.
The feed-back circuit is connected to receiver circuit as a master-Slave nd checks the feedback nd sends it back to the HUB
This way the HUB comes to know in real time if the command has been completed and the volume at which the music is playing.
-If the HUB doesn’t receive a feedback, it raises an alarm which is resetted if the f/b for nxt command is received.
In case the feedback

## Slide 4: Music-Controller Node
Controls the volume of the music-player, Turns it ON & OFF and also retrieves the feedback about the music from the music player.
Components used :
    2 ATTiny 85 Micro-controller or an arduino uno
    RF Receiver 344MHz
    RF Transmitter 315MHz
    Sensor (microphone Amplifier circuit)
    Music player
    Infra-red transmitter
Divided into two parts:
1) Receiver and Controller circuit | 2) Sensing and Feedback circuit

## Slide 5: Features
Real time feeback so that you know each and every detail of your house even if you are away.
Real time feedback after every command to let you know if what you wanted has been actually achieved.
Alarm raised if no feedback received.
Inherited Advantages of Star topology.
Flexibility to choose from various ways of getting things done.
Notes: Advantages of star topology:

## Slide 6: Testing & Real Time Analysis
This is the encoded command received from the server
This is after decoding the command
This is the feedback received from the device
Feedback is 69% brightness
Feedback is 23% brightness
Feedback is 2% volume
Feedback is 0% volume
Test result for light node
Test result for music node

## Slide 7: Mic. As a SENSOR
With RMS & AVERAGE
JUST RMS

## Slide 8: TESTING
100% Volume
25% Volume
75% Volume
50% Volume

## Slide 9: LDR As a SENSOR

## Slide 10: Testing nd debugging